# Text boxes

GAME SET

"Time-point"

PRODUCT'S PASSPORT

Smolensk

1. Description

"Time-point" game set is designed to be used in different laser tag game scenarios.

2. Application

"Time-point" game set can be used practically in many team games scenarios ( as a virtual flag point or control point).

3. Package set

- "Time-point"	- 1 piece.

- Product's passport	- 1 piece.

4. Basic technical specifications

| Height, mm | 320 |
| --- | --- |
| Width, mm | 230 |
| Power-supply voltage, V | 7.4 |
| Battery capacity, A/h | 3.0 |
| Weight, kg | 1.2 |

5. Design

"Time-point" game set is made of impact resistant plastic, the power battery is installed in the lower part and the control units are located in the upper part of the device.

6. Maintenance

It's important to take good care of all parts of the game set so that the equipment can function properly. Protect IR diode from getting dirty or damaged. Don't let entry of liquids inside the case. Charge the battery timely. The game set is charged by a charger intended for lithium batteries (a charger is not included in the game set and must be purchased separately). Avoid hitting the device.

7. Instructions for use

"Time-point" game set is activated by a key, the switch slot is located on the upper panel of the device. OLED display shows current information concerning the working mode of the device, the settings and the game progress. The buttons on the front panel are used for adjusting the settings, selecting game scenarios and starting the game.

Three game scenarios are available to be chosen: "The Time Gate", "Time Robbers", "War of the Worlds".

Parameters of game scenarios are set in the scenario settings menu.

The control interface is intuitive, the key moments are duplicated by voice prompts.

2

3

8. Warranties

The manufacturer guarantees operational reliability of the "LASERWAR" individual game set if the customer observes the rules of the correct operation. The warranty period for technical support is 12 months starting from the date of the purchase. The manufacturer undertakes to replace or repair the equipment of an individual game set free of charge, subject to the customer's observance of transportation, storage and operation rules and paid delivery of faulty equipment to Smolensk.

The warranty period for batteries, speakers and IR modules is 14 DAYS. These accessories are consumables.

ATTENTION! The warranty shall not cover the batteries in case of improper use (charging them with an inappropriate type of charger)!

9. Contact information

______________________________________

Rules for operating the equipment

1. Weather conditions During the production process, the equipment is tested for performance under various weather conditions. Despite this, we strongly recommend not to use the equipment in rainy weather and at temperatures below -20°C.

What do you need to know when operating game sets in unfavorable weather conditions?

The most important thing is not to allow moisture to enter inside the device. If this has happened, stop operating the device and dry the equipment at room temperature for at least 2 hours.

2. Power supply. Lithium batteries with a nominal voltage of 7.4 V are used as power source in the "Time-point" game set.

The batteries must be charged under supervision for no longer than 3 hours.

The device must be stored in a well-ventilated room at a temperature from +18°С to +30 °С and with relative air humidity of 45-65%.

The warranty period for batteries, speakers and IR modules is 14 DAYS. These accessories are consumables.

ATTENTION! The warranty shall not cover the batteries in case of improper use (charging them with an inappropriate type of a charger)!

5

4

Dear customer!

On the behalf of OOO "Lasertag" company we are happy to welcome you and thank you for choosing our products, we are confident that the product which you have purchased from us will bring you pleasure and last for a long time. This warranty card establishes a warranty liability for the product to the extent provided by the Law of the Russian Federation "On the Protection of Consumer Rights".

This warranty card is valid for 12 months from the date of purchase of the product, subject to the compliance of the terms of the warranty.

Warranty terms:

1. The warranty becomes effective upon presentation of this warranty card where the serial number of the product and the date of its purchase confirmed by the service center shall be indicated.

2. These warranty obligations apply to products purchased only from an official representative of OOO "Lasertag" company or its Official Dealer.

3. This warranty is not valid if the faults in the product have been caused by:

- failure to follow the Instructions for use;

- mechanical damage;

- entry of foreign objects, liquids, etc. into the product;

- animal activities;

- unauthorized access to the units and parts of the product by persons not authorized to perform these actions;

- use of the product for purposes other than those it has been designed for;

- force majeure (natural disaster, fire, accident, etc.);

- the product's breakdown due to improper connection, faulty power supply and / or poor care of the product.

4. In case an original warranty card is lost, a duplicate can not be issued.

Information on repairs performed during the warranty period (to be filled out by workers of the service center where the warranty repair service is provided).

| Date:__________________ Performed works: _____________________________________________________________________ Service center's stamp | Date:__________________ Performed works: _____________________________________________________________________ Service center's stamp |
| --- | --- |
| Date:__________________ Performed works: _____________________________________________________________________ Service center's stamp | Date:__________________ Performed works: _____________________________________________________________________ Service center's stamp |
| Date:__________________ Performed works: _____________________________________________________________________ Service center's stamp | Date:__________________ Performed works: _____________________________________________________________________ Service center's stamp |

7

6