# Text boxes

LIMITED LIABILITY COMPANY LASERWAR

SPECIFICATION

CHECKPOINT

Additional Device

Smolensk

1. Description

The checkpoint (ChP) is an additional gaming device that can be used in various game scenarios.

2. Scope of application

The device is intended for the scenario "Capturing a checkpoint" and is used in organizing laser tag events, tactical training, corporate and entertainment events.

3. Package Contents

1. Digital control point RGB - 1 pc.

2. Product specification - 1 pc.

4. Basic technical data

| Height, mm | 580 |
| --- | --- |
| Diameter of pipe, mm | 110 |
| Diameter of the base, mm | 240 |
| Type of battery used | Lithium |
| Battery capacity | 2200 mAh |
| Charger type | Smart Li + |
| Number of photo sensors, pcs. | 1 |
| Number of IR diodes, pcs. | 1 |
| Weight, kg | 1.5 |

5. Device

The RGB checkpoint consists of a black plastic tube covered with a protective color cloth, a base at the bottom of the casing, one

LED ribbon of different colors, power socket and administrator button.

The main body is a structure in which the battery is installed, control units, module fastening elements, a protective glass, as well as a siren sound element.

6. Instructions for use

The control point is started with the button and after a couple of seconds is activated - the LED ribbon blinks white light. Capture is carried out by firing a laser tag of weapons inside the ChP from a close distance (no more than 1 meter). When you capture a ChP from one of the teams, it starts to glow with the color of the invader's command, and also produce a sound. After a predetermined period of time (from 2 to 60 minutes), when the counter of holding the ChP of one of the commands reaches a maximum value of 50% + 1 second of time, the ChP flashes and turns on the siren for 10 seconds. The time intervals vary with the help of a special administrative button on the ChP case.

To reboot the ChP, you can use a conventional remote control for laser tagging weapons or simply restart the power.

7. Changing the settings

In ChP, a new convenient way of changing the operating time through the button on the housing is implemented. The retention time of the QD can be set in the interval from 2 to 30 minutes (2, 4, 6, 8, 10, 20, 30). To set the capture time, you need to lock the admin button on the case when turning on the power of the ChP; You will hear a beep and only then you can set the time by pressing the Admin button. Each pressing of the button is accompanied by a change in the capture-hold time of the ChP.

The color of the RGB tape will vary depending on the selected mode. The ribbon colors correspond to the following values ​​(in minutes):

Red - 2 Yellow - 4 Green - 6 Blue - 8 Blue - 10 Purple - 20 White - 30 min

By default, the round is 4 minutes, the color is yellow. To save the selected mode, again press and hold the "admin" button for a few seconds, the point will remember the selected parameter.

2

3

8. Contact information

Official site:

Www.laserwar.ru

Email:

Info@laserwar.ru

Support@laserwar.ru       Date of purchase:_______________

Skype:

info-laserwar.ru

support-laserwar.ru

______________________________________

Rules of operation of equipment

1. Weather conditions. In the production process, the equipment is tested for operation under various weather conditions. Despite this, we strongly do not recommend using the equipment in rain and temperatures below -20 ° C.

What you need to know when operating gaming kits in adverse weather conditions?

Most importantly, avoid getting moisture inside the device. If this happens - stop operation, dry the equipment at room temperature for at least 2 hours.

2. Power source. As a power source in the "RGB Digital Check Point" game set, we use lithium batteries with a capacity of 2.2 Ah

To recharge the batteries, you must use a Li + battery charger and a Smart Li +

Store the equipment in a well-ventilated place at a temperature of +18 °C to +30 °C and relative humidity of 45 to 65%.

On the batteries, speakers, IR modules, the warranty is 14 DAYS. These accessories are consumables.

ATTENTION! In the event of improper use of batteries (charging by an inappropriate type of charger), the battery warranty does not apply!

5

4

Dear customer!

LLC "Lasertag" welcomes you and thanks you for choosing our products, and also expresses confidence that the product you purchased will bring you pleasure and will last a long time. This coupon establishes a warranty liability for the product in the amount provided by the Law of the Russian Federation "On Protection of Consumer Rights".

This warranty card is valid for 12 months from the date of purchase of the product subject to the terms of the guarantee.

Terms of guarantee:

1. The warranty becomes effective upon presenting this coupon, which indicates the serial number of the product and the date of purchase, confirmed by the service center.

2. These warranty obligations apply to products purchased only from the official representative of OOO "Lasertag", or its Official Dealer.

3. This warranty is void if defects in the product have occurred in the event of:

- non-observance of Instructions for use;

- mechanical damage;

- ingress of foreign objects, liquids, etc .;

- animal activities;

- unauthorized access to the units and parts of the product of persons not authorized to carry out the specified actions;

- use of the product for purposes for which it is not provided;

- acts of force majeure (natural disaster, fire, accident, etc.);

- failure of the product due to incorrect connection, a faulty electrical outlet and / or poor maintenance of the product.

4. If the warranty card is lost, a duplicate is not issued.

Information about the repairs carried out during the period of guaranteed service (to be filled in by the service center performing the warranty repair)

| Date:__________________Completed work: _____________________________________________________________________ Printing Service Center | Date:__________________ Completed work: _____________________________________________________________________ Printing Service Center |
| --- | --- |
| Date:__________________Completed work: _____________________________________________________________________ Printing Service Center | Date:__________________Completed work: _____________________________________________________________________ Printing Service Center |
| Date:__________________Completed work: _____________________________________________________________________ Printing Service Center | Date:__________________Completed work: _____________________________________________________________________ Printing Service Center |

7

6